## Slide 1: Component-based Design of Embedded Systems with FPGA Support
R. Schönecker, Z. Křivka, D. Kolář
UIFS, FIT, VUT Brno, CZ
ASIS 2007, Sv. Hostýn

## Slide 2: Notions
ES = Embedded System
  Non-standard or missing user I/O
  autonomous
  Eg. Coffeemaker, Fridge, Cell-phone, Car
MCU = MicroController Unit
  MCU in the middle, Programmable: code
FPGA = Field-Programmable Gate Array
  Programmable: HW (& code)

## Slide 3: Motivation
Create virtual laboratory for embedded system developers (MCU board vs. FPGA boards)
FPGA-developement – cheaper, flexible
  Dynamic reconfiguration  many architectures
  Lower HW cost during developement and testing
How to introduce FPGA to ES developer
  Common approach: MCU+peripherals (1 arch.)
  FPGA approach: FPGA+(CPU)+peripherals (n arch.)
  Combination?

## Slide 4: Tools
Processor Expert (PE) by Unis
  Component = Embedded Bean (EB)
  Higher abstraction (not only encapsulation, but adds common/unified interface) – change of the type of MCU without change of the code
    conceptual approach, 1 architecture
Xilinx tools EDK, ISE
  FPGA developement (many arch.)
  Component = IP core (only encaps., info needed)

## Slide 5: Integration
Master (MCU; PE) – Slave (FPGA+(CPU); Xilinx) (coprocessor)
FPGA as peripheral in PE
Support the FPGA+CPU platform in PE
Synthesis, implementation and bit-stream download into FPGA still by Xilinx tools.

## Slide 6: Production Flow PE with FPGA
Design entrance (PSF, EB-Wizard)
Insert new EB for FPGA-components (corresponds to IP cores) into PE
Target-Platform Generation, Compilation
Synthesis of FPGA design, Download

## Slide 7
IP Core Beans
Repository
Design Entry Generator
HDL
HW Platform Specification
Xilinx Design Flow
Embedded Beans
Repository
Design Entry
Compilation & Implementation
IP Cores Repository
Design Entry
Design Synthesis
Design Implementation
Download to Device
Processor Expert Design Flow
Simulation
functional and timing verification
static analysis
in-circuit verification
new development iteration
Figure 1: Combined Design Flow
CPU
FPGA

## Slide 8: General Run-Time Interconnection

## Slide 9: Evaluation and Problems (V1)
General purpose usage, not practical
PROBLEM: slow and long latences of general communicational interfaces (UART, USART, SPI)
Solution 1: integration into 1 chip/board
Solution 2: V3  create PE models for basic architectures used in FPGA developement  integration of Xilinx tool into PE‘s production flow

## Slide 10: Conclusion
PROBLEMs:
  Knowledge base for automatic FPGA-platform specification generation and half-automatic components interconnection
Simulation and verification tools only just before finish line
This work has been supported by the Czech Ministry of Education, Youth and Sports grant MŠMT 2C06008 "Virtual Laboratory of Microprocessor Technology Application".