## Slide 1: Continuous-time signals I.
Honza Černocký, ÚPGM
Please open Python notebooks continuous_1, fs, ft

## Slide 2: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 3: Remember lecture 1 … functions and sequences
Signals with continuous time (analog, real world) are defined for all times t. Signály se spojitým časem, spojité signály.
  From math point of view, they are functions x(t)  round brackets
Signals with discrete time (computer, digital world), sampled signals are defined only for integer times (sample numbers) n. Signály s diskrétním časem, diskrétní signály, vzorkované signály.
  From math point of view, they are sequences x[n]  square brackets.

## Slide 4: Continuous time signals
Time (horizontal axis) is in seconds [s]
Frequencies will be true ones - in 1/s – Hertz [Hz]
Continuous–time signals are really defined for all times.
When plotting, we’ll use some small time-step and we’ll definitely use plot.
Reminder – for discrete-time signals, we either emphasized that they are discrete and used stem, or did not care and used plot.
#continuous_plotting
When generating a signal in Python (or any other programming language), you can advantageously use indexing by results of conditions.
#use_conditions

## Slide 5: Time modifications of continuous signals
Reversal of the time axis (otočení): y(t) = x(-t)
Basic time shifts
  Delay (zpoždění) – shift to the right: y(t) = x(t – τ)
  Advance (předběhnutí) – shift to the left: y(t) = x(t + τ)
Reversal of the time axis and time shifts:
  Reversal and shift to the right: y(t) = x(-t + τ)
  Reversal and shift to the left: y(t) = x(-t - τ)
Unsure ? Run a check:
  Select an important event in the signal
  For the modified signal, evaluate the time modification for this event
  Look at the resulting time in the original signal.
    Same event as in the modified one ? OK
    Different event ? BAD, DO IT AGAIN
#time_modifications

## Slide 6: Modifying the speed of time …
Contraction of time (kontrakce, zrychlení času): y(t) = x(mt) for m > 1 – everything will run faster
Dilation of time (dilatace, zpomalení času): y(t) = x(mt) for m < 1 – everything will run slower.
We rarely manage to slow-down or speed-up time in real world, but we can use this know-how to compute / draw a faster or slower signal provided we know the original one.
#time_contraction_dilation

## Slide 7: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 8: Constant signal
Discrete: x[n] = const
Continuous: x(t) = const
Constant signals are very useful – remember charging your cell phone 
Constant signal has zero frequency.
#constant_signal

## Slide 9: Unit step (jednotkový skok) and unit pulse (jednotkový impuls) – discrete
Unit step: all samples below n = 0 are zero:
Unit pulse: all samples except n = 0 are zero:
Unit pulse can be given as a difference of basic and shifted unit steps: δ[n] = σ[n] - σ[n-1]
#discrete_unit_step_pulse

## Slide 10: Unit step in continuous time
Unit step: signal below t = 0 is zero:
Unit pulse should be defined as:
But it is hard to derive unit pulse, as the derivation in t = 0 is not defined.
Therefore, we define approximate (smooth) unit step with width Δ and derive it:
#unit_step_derivation

## Slide 11: Dirac pulse (Diracův impuls)
The surface – “mighteness” (mocnost) is
We run Δ to zero, and we obtain the Dirac pulse:
  The width is zero, the value is infinity.
  The surface is however still one
Mathematicians often refuse to call this a function, and rather call it distribution.
We usually plot it with as a square with an arrow going to “infinity”.
Dirac pulse can not be generated – it is a (very useful!) theoretical construct
#dirac

## Slide 12: The sampling property of Dirac pulse
Dirac is relatively aggressive when multiplied with signal x(t): it sets everything to zero, except t = 0.
When integrated, the output value is x(0): the signal got sampled:
In case we shift the Dirac pulse to time τ, we obtain similar behavior
We will use this property when explaining the sampling.
#dirac_sampling

## Slide 13: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 14: Periodic signals - continuous
Periodic signals have repetitive behavior …
We can find such T, that x(t + T) = x(t)
T is called period, but several T’s can exist …
T1 is the smallest one, we call it fundamental period (základní perioda).
Periodic signals have fundamental frequency (základní frekvence) in 1/s (Hertz, Hz):
We often work with angular/circular frequency/velocity (kruhová/úhlová frekvence/rychlost)
#periodic_continuous

## Slide 15: Periodic signals - discrete
We can find such N, that x[n + N] = x[n],
N is called period, but several N’s can exist …
N1 is the smallest one: fundamental period (základní perioda).
Periodic signals have fundamental normalized frequency (základní normovaná frekvence) in []:
We often work with normalized angular/circular frequency / velocity (normovaná kruhová/úhlová frekvence/rychlost)
Conversion from N1 to f1 and ω1 is straightforward, but not vice versa.
#periodic_discrete

## Slide 16: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 17: Instantaneous power of a signal
Remember Ohm’s law:
Therefore, we define instantaneous power (okamžitý výkon) for both discrete and continuous signals as:
Magnitude is not needed when we work with real signals, but we should not forget it for complex ones … and we do have complex signals in ISS !

## Slide 18: Energy and powers of signals
Energy (energie) is given as a sum (discrete signals) or integral (continuous signals) of instantaneous power over a time interval:
Mean power (střední výkon) is normalized by the length of the time interval:
Root mean square value (efektivní hodnota) is the magnitude of a d.c. signal with equivalent power:
#powers

## Slide 19: Powers of periodic signals and of a cosine
When determining power of periodic signals, it is wise to compute over (and normalize by) one period: N1 (discrete) and T1 (continuous ).
Computing power of a cosine is a basic task: T1 and angular frequency ω1:
With the help of basic formula , we can express the power as
The integral of any number of periods of cosine is 0, so the power is:
#cosine_power

## Slide 20: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 21: What do we require ?
From any spectral analysis, we want to know
  Where are the frequencies in the signal
  How strong is the signal at a given frequency – “how much”
  What is the phase of the signal at a given frequency – “how shifted”.
We now have a periodic signal and we have seen that it can be composed of
  The d.c. value
  The slowest component (fundamental frequency)
  Harmonically-related components at multiples of this frequency: kω1
We will define Fourier series (Fourierova řada)
  It is series, not a function, we will work with coefficients !
  They will “sit” on a given frequency.

## Slide 22: Real formulation of FS
We could write FS as a real function
  c0 is D.C. component
  Ck is magnitude at frequency kω1
  Φk is phase at frequency kω1
But this would make the computation of coefficients quite complicated
  remember the problems with phase of cosine each time we tried to use them for analysis …

## Slide 23: Complex formulation of FS
Complex form of FS is more practical and more frequent:
  c0 is D.C. component
  ck is a complex coefficient belonging to frequency kω1
    Its magnitude |ck| determines the “strength” of signal at given frequency
    Its phase arg ck determines the “shift” of signal at given frequency.
    We need ck at kω1 and c-k at -kω1 to sum up to one real cosine – same trick as we used for DTFT.
The formula above is called synthesis formula
The values and positions of coefficients ck are called spectrum (remember “spectrum” is a generic term).
They are complex, so we will need 2 plots: magnitude and phase.

## Slide 24: Relations between the real and complex forms
The conversion is easily done by breaking cos into a sum of two complex exponentials:
After re-arranging:
So we see the conversion real -> complex and vice versa:
For real signals x(t), there must be a symmetry of coefficients:
#cos_complex_exp

## Slide 25: Computation of FS coefficients – analysis formula
By FS, we are actually decomposing the signal (projecting, computing similarity with, computing correlation with) into bases
We know that the projection can be done by a scalar product of the signal and the analysis signal.
  Discrete: Continuous:
The signal is periodic, so it makes sense to integrate only over one period T1 picked wherever we want:
  0 to T1, or -T1 /2 to T1 /2 or …
FS basis
  is complex, so we need to take it in complex-conjugate form.
  has norm T1, (just try to compute the integral of its magnitude over one period T1), so we need to divide by T1.

## Slide 26: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 27: Examples of FS computation
Examples
  x(t) is complex exponential
  x(t) is a cosine with magnitude and phase.
  x(t) is a sequence of rectangular pulses
Computing FS – always respect the rule of maximum laziness !
  Looking at the definition formula – can’t I find the FS coefficients directly ?
  Integrating by hand (for “simple” deterministic signals, such as the rectangular pulses).
  Integrating numerically – see next lecture, it will lead us to DFT.
Exercise your intuition
  Slow changing signal has little high frequencies – few non-zero FS coefficients, narrow spectrum
  Fast changing signal has lots of high frequencies – lots of non-zero FS coefficients, wide spectrum
  An edge or pulse in the signal is a very fast change !

## Slide 28: FS of a complex exponential and cosine
Plain complex exponential:
  This is the simples case, as we can directly relate it to the synthesis formula. c1 = 1, and it “sits” at ω1
Complex exponential multiplied by a constant:
  Dtto, the coefficient is the constant
Examples for ω1 = 2000π rad/s
#fs_complex_exp
Cosine with a magnitude and phase
We have seen that we can break it into two complex exponentials at ω1 and at -ω1
#fs_cos

## Slide 29: FS of a series of rectangular pulses
Period T1 , height D and width of pulses ϑ.
  The ratio ϑ / T1 is called “duty cycle” (střída)
We will need to do some integration here … but first some intuition:
  There are sharp edges, so the spectrum will have lots of high frequencies.
  Narrow (fast) pulses will lead to even broader spectrum
  Wide (slow) pulses will lead to narrower spectrum

## Slide 30: Preparation I – cardinal sine
Cardinal sine is defined as
At zero, the fraction is not defined, so we define “by hand” sinc(0) = 1.
Also called “Mexican hat” function.
We will soon need to plot this function as complex numbers – split into magnitudes and phases.
#sinc – beware of difference between numpy’s and my definition !

## Slide 31: Preparation II – integral of ejxy
We will soon need a finite integral
  Dubbed “Euler’s integral” or “Šebesta’s tool” (Šebestova pomůcka - ŠP)
Some operations (primitive function, using and multiplying by b/b):
We can verify that it works also for x = 0, therefore:

## Slide 32: Now finally ready for FS coefficients of the sequence of rectangular pulses …
By definition:
But it is enough to integrate from –ϑ/2 to +ϑ/2:
And apply ŠP:
Now we could use our favorite mathematical program (Python, Excell) and let it stem the coefficients, but let us go step-by-step.

## Slide 33: FS coefficients of the sequence of rectangular pulses – step 1
Let us start with an auxiliary function (pomocná funkce) with any angular frequency ω.
This function will intersect axis ω for argument of the function equal π (and its multiples)
That is for frequency and its multiples.
#fs_rectangles_auxiliary
… note the split of real cardinal sine into magnitudes and phases
  positive real number a has magnitude a and phase zero (or, for masochists, any multiple of 2π).
  Negative real number -a has magnitude a and phase +π or - π (or, for masochists, any odd multiple of π…).
  We can pick phase π or –π voluntarily, but we will try to have positive ones for positive values of x and negatiove ones “on the left”

## Slide 34: FS coefficients of the sequence of rectangular pulses – step 2
When the auxiliary function is ready, we can fill the FS coefficients under it – at multiples of the fundamental angular frequency ω1.
Note that one coefficient ck is given by both its magnitude and phase, therefore, we need to look into both plots.
#fs_rectangles_full
An example for f 1 = 1 MHz, i.e. T 1 = 1 μs, ω1 = 2x106 π rad/s = 2M π  ϑ = T1 / 2, so that the duty cycle is 50%. Height D = 6.
#fs_rectangles_1Mhz
… note that as ωx = 2 ω1, only odd coefficients are non-zero (plus c0).

## Slide 35: Synthesizing sequence of rectangular pulses from FS coefficients
We take the synthesis formula and keep adding components
Starting with k = 0: the d.c. component
Then going in pairs of coefficients ck and c-k to ensure that we are always adding cosines.
Omitting even coefficients k as the corresponding coefficients ck are zero.
#fs_rectangles_1Mhz_synthesis

## Slide 36: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 37: Simples changes of the signal
Changing the D.C. offset y(t) = x(t) – 3: only ck changes
Making the signal negative y(t) = -x(t): all coefficients ck go negative
  The magnitude does not change
  Phase will change from +π or –π to zero and vice versa.
Faster signal y(t) = x(2t): the whole spectrum will be wider, but the same values of ck !
Narrower pulse ϑ = T1 / 4, duty cycle 25%, otherwise the same:
  the auxiliary function will be wider (as smaller ϑ leads to wider lobes (laloky)) of the cardinal sine.
  The multiples of ω1 will be the same as before.
  The coefficients will be smaller (signal “working less”).
#fs_rectangles_1Mhz_zero_dc
#fs_rectangles_1Mhz_minus
#fs_rectangles_1Mhz_faster
#fs_rectangles_1Mhz_narrower

## Slide 38: Shifts of signal
In case the signal is delayed y(t) = x(t-τ):
We can perform a change of variable g = t – τ and show that:
But this is the original coefficient multiplied with a “correction”:
Behavior in magnitudes and phases:
  Magnitudes do not change:
  Phases change by subtracting a linear function with slope –τ
#fs_rectangles_1Mhz_delayed #fs_rectangles_1Mhz_advanced

## Slide 39: Power from FS – Parseval’s theorem
Remember that the power of periodic signal can be obtained:
And we can have the signal represented by the FS synthesis formula:
We will be able to obtain the power also by summing the powers of individual complex exponentials:
Integration of a constant over T1 is this constant multiplied by T1, so:
- power can be obtained from FS.

## Slide 40: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 41: Fourier transform (Fourierova transformace) – what do we want
We want to analyze also non-periodic signals.
We are asking three usual questions:
  Where will be the frequencies ? For non-periodic signals, we can not determine fundamental frequency ω1 and its multiples => we will need to process the whole frequency axis ω
  The result will not be coefficients, but a spectral function (spektrální funkce) X(jω).
  “How much ?” will be answered by the magnitude of spectral function |X(jω)|
  “How shifted ?” will be answered by the phase of spectral function arg X(jω).

## Slide 42: Definition of FT
Direct FT (from time to frequency):
Inverse FT (from frequency to time):
We can also denote it as:
For real signals, as usual, we obtain a symmetrical spectrum:
As before, we are intrigued by this j in notation – why not simply X(ω) but X(jω) ?
  Remember the DTFT case – for discrete signals, we did not denote it X(ω) but X(ejω) !
As we are getting more experiences in frequency transforms, we note that direct and inverse transform look very similar, except for the sign.

## Slide 43: How did we get here ?
Trying to derive FT from FS by “diluting” periodic signals… push T1 to infinity …

## Slide 44
Does not really work, as the with more and more diluting, the coefficients are smaller and smaller
for T1 = ꝏ, they become zero 

## Slide 45: FS to FT correctly …
We depart from the definition of Fourier series:
We modify for in a smart way:
  ck will become an infinitely small increment of FS coefficient dc
  the limits of integral will become –ꝏ and +ꝏ.
  ω1 will not become zero, but an infinitely small increment dω
  with it, we can eliminate the period so
  kω1 will become any angular frequency ω.
When done, we obtain:
But calling the result “infinitely small increment of FS coefficient over infinitely small increment of angular frequency” would be stupid => spectral function.

## Slide 46: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 47: FT of Dirac pulse δ(t)
Remember that we defined the sampling property of Dirac pulse:
When standing in the definition of FT, it samples the complex exponential at t = 0.
The integral is thus reduced to

## Slide 48
and the result is X(jω) = 1. This is a constant for all frequencies
  Magnitude 1
  Phase zero.
Intuition check: Dirac pulse is a very fast signal, so it should have a very wide spectrum.

## Slide 49: FT of shifted Dirac pulse δ(t - τ)
Using again the sampling property:
We will work only around time τ:

## Slide 50
and the result is For this expression:
  Magnitude is 1
  Phase is linear with slope –τ:
Intuition check: shifted Dirac pulse is still a very fast signal, so it should have a very wide spectrum.

## Slide 51: FT of a D.C. signal
Signal equal to a constant: x(t) = A.
Without derivation, we set X(jω) = 2πA δ(ω) and check that it is correct.
Dirac pulse has sampling property even in frequency, so the result will be
Therefore, x(t) = A.
Intuition: a very slow signal should have a very narrow spectrum.

## Slide 52: FT of a complex exponential
For
We define and we check again …
Intuition: a signal that has only one frequency should have a very narrow spectrum only at this frequency.

## Slide 53: FT of a periodic signal decomposed by FS
A periodic signal with fundamental period T1 and angular frequency ω1 can be decomposed by Fourier series:
… and we learned that one complex exponential has spectral function
As all Fourier transforms, FT is linear, so the resulting spectral function will be series of shifted Dirac pulses, each multiplied by 2π and the respective coefficient of FS:
We will be using this trick when deriving the spectral function of a sampled signal.

## Slide 55: Rectangular pulse and its FT
Similar definition as above, but this time, the pulse is not periodic.
height D and width of pulse ϑ.
We will again need to do some integration here … but first some intuition:
  There are sharp edges, so the spectrum will have lots of high frequencies.
  Narrow (fast) pulse will lead to even broader spectrum
  Wide (slow) pulse will lead to narrower spectrum
Using FT definition

## Slide 56: Spectral function of rectangular pulse
Making use of Šebesta’s tool with
We obtain
… cardinal sine again, but this time it is the ultimate result, not an auxiliary function.
We are again interested, where does sinc touch the frequency axis, we set: and find - same as for FS.
Plotting again as magnitude and phase, and “beautifying” the plot by using +π for positive frequencies and –π for negative ones.
#ft_rectangle

## Slide 57: Signal with a square spectral function
Let’s try an inverse exercise … rectangular spectral function
Same process as above, but we need to run inverse FT:
Making use of Šebesta’s tool with
We obtain
The cardinal sine will intersect t axis for:
#ift_of_rectangular_spectral_function

## Slide 58: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 59: Properties of FT
We will use rectangular pulse with parameters: ϑ = 0.5 μs and D = 600000 (to get reasonable values of spectral function).
#ft_rectangle_0.5us

## Slide 60: Linearity and inversion
FT is linear, in case we have independently
The FT of mix:
is exactly the same mix of original spectral functions:
Proof:
#ft_linearity
For inversion of signal: , we obtain the same inversion of spectral function:
  The magnitude does not change
  Phase will change from +π or –π to zero and vice versa.
#ft_negative

## Slide 61: FT of a delayed signal
In case the signal is delayed y(t) = x(t-τ):
We can perform a change of variable g = t – τ and show that:
But this is the original spectral function multiplied with a “correction”:
Let us study the behavior in magnitudes and phases:
  Magnitudes do not change:
  Phases change by subtracting a linear function with slope –τ:
#ft_rectangles_0.5us_delayed

## Slide 62: FT of time-contracted or time-dilated signal
Modifications of the time axis: speeding up (contraction) for m > 1, slowing down (dilation) for m < 1
By definition
Without derivation:
Interpretation:
  For m > 1 (narrower signal), the spectrum should be wider and smaller (less signal to work)
  For m < 1 (wider signal), the spectrum should be narrower and bigger (more signal to work)
#ft_rectangles_0.5us_contract_dilate

## Slide 63: Energy from FT – Parseval’s theorem
The total energy of signal is given by (don’t try this for periodic or constant signals …)
We can try it with one x(t) let intact and another given by IFT:
By changing the order of integrations:
Square bracket is a weird FT, actually the value of spectral function for X(-jω) !
Knowing that we can:
is called two-sided energy spectral density #energy_density

## Slide 64: Agenda
Basic information, operations with time
Important signals – with links to discrete ones
Periodic signals
Energy and power
Spectral analysis of periodic signals – Fourier series
FS of typical signals
Properties of FS and power by FS
Spectral analysis of non-periodic signals: Fourier transform
FT of typical signals
Properties of FT and energy by FT
Summary

## Slide 65: SUMMARY I
Continuous-time signals are defined for all times … but we can always fake it
  In plotting by using plot
  In computing by using numerical integration (sum of values multiplied by time-step)
In addition to known time operation, we can speed-up or slow-down the time axis.
Unit step and Dirac pulse are non-existing but very useful signals, Dirac has:
  zero width, infinite size, surface one
  very useful for sampling things.
Periodic signals repeat
  the smallest repetition time is called fundamental period.
  and its inverse (both in continuous and in discrete time) is fundamental frequency.
Energy and power are just sums or integrals of squarred signal values
  raw for energy
  normalized by length for power

## Slide 66: SUMMARY II
Spectral analysis of periodic signals: Fourier series (FS)
  the result are complex coefficients sitting at multiples of fundamental frequency, must be plotted two plots: magnitude and phases.
  two opposite coefficients are complex conjugate and make up for one cosine.
  they are computed by projecting the signal on complex exponentials.
FS of typical signals
  complex exponential has one FS coefficient.
  cosine has two FS coefficients.
  sequence of rectangles has infinity FS coefficients, decaying towards high frequencies according to cardinal sine.
Properties of FS
  when the signal is shifted, nothing happens to the magnitudes, phases go downhill (delay) or uphill (advance)
  in case the signal is contracted (dilated) the values of FS coefficients are the same, but they "sit" at different frequencies.
  power can be computed from FS coefficients (Parseval).

## Slide 67: SUMMARY III
Spectral analysis of non-periodic signals: Fourier transform (FT)
  the result is spectral function defined for all frequencies
  spectral function is computed by projecting the signal on complex exponentials.
Typical signals
  Dirac has constant spectral function with flat (Dirac at zero) or inclined phase (Dirac not at zero)
  spectral function of a D.C. signal is Dirac.
  spectral function of a complex exponential is shifted Dirac.
  periodic signal can be broken by FS which can be converted to Diracs at multiples of fundamental frequency.
  rectangular signal has spectral function given by cardinal sine.
  dtto in the inverse direction: signal corresponding to square spectral function is cardinal sine.
Properties of FT
  FT (and FS) is linear
  FT of a delayed signal has the same magnitude, phase shifts downhill (delay) or uphill (advance)
  FT of time contracted signal goes in the opposite way: wider for narrower signal, narrower for wider signal.
  Energy of a signal can be obtained from its FT (converted to energy spectral density).

## Slide 68: Basic truths on signals and spectra
Spectrum of periodic signal is discrete (coefficients) – Fourier series
Spectrum of non-periodic signal is continuous (function) – Fourier transform
Spectrum of narrow (fast) signal is wide.
Spectrum of wide (slow) signal is narrow.
Any sharp edge will result in infinitely long spectrum.
Spectrum of delayed signal has the same magnitude as before, phase goes downhill.
Spectrum of advanced signal has the same magnitude as before, phase goes uphill.
Time and spectral domains are like fire and water: always do the opposite things!